## Slide 1
VHF 2m
144-146MHz (2MHz band)
Satellite Downlink
144.050 CW calling
144.300 SSB Center
144.025
144.500
144.794
144.975
145.806
Satellite exclusive
145.800 ISS
145.575
Repeater out
145.206
145.500 FM Calling
144.800 APRS
145.194
Repeater in
Space Comm
145.794
Space Comm
UHF 70cm
430-440MHz (10MHz band)
See verso
20 kHz
12 kHz
None
 | Authorized Peak Envelope Power (PEP) per class (W) |  |  | 
 | I | II | III | IV
VHF - 2m | 400 | 200 | 100 | 50
UHF - 70cm | 200 | 100 | 50 | 30
IARU Region 1
2m & 70cm Band Plan
Based on IARU-R1 VHF Handbook v9.00 November 2020
Ver 1.1
Sources:
National Authority for Management and Regulation in Communications of Romania - Radio amateur services regulations
ITU Radio Regulations, 2020 Edition
IARU-R1 VHF Handbook
YO3MIO - Feel free to print, distribute and modify this document while maintaining the source and author https://github.com/mircea84/VHFHamBands/
1 430.000 - 431.200 MHz not part of radio amateur service
432.493
432.100
432.400
Repeater in (7.6MHz shift)
Repeater in (1.6MHz shift)
432.500 New APRS
433.500 FM call
433.450 Digital voice call
433.400 SSTV
Repeater in (25kHz ch. / 2MHz shift)
Repeater out
(25kHz ch. / 1.6 or 2MHz shift)
Satellite service
Repeater out (7.6Mhz shift)
Repeater in (25kHz ch. / 1.6MHz shift)
Repeater out (1.6MHz shift)
431.2001
432.000
432.500
433.000
433.600
435.000
438.000
430.375
431.625
431.050
434.600
439.425
438.650
434.790
All modes
CW
MGM
SSB
FM / Dig. voice
Sat. service
ISM

## Slide 2
VHF 2m
144-146MHz (2MHz band)
Satellite Downlink
144.050 CW calling
144.300 SSB Center
144.025
144.500
144.794
144.975
145.806
Satellite exclusive
145.800 ISS
145.575
Repeater out
145.206
145.500 FM Calling
144.800 APRS
145.194
Repeater in
Space Comm
145.794
Space Comm
UHF 70cm
430-440MHz (10MHz band)
See verso
20 kHz
12 kHz
none
 | Authorized Peak Envelope Power (PEP) per class (W) |  |  | 
 | I | II | III | IV
VHF - 2m | 400 | 200 | 100 | 50
UHF - 70cm | 200 | 100 | 50 | 30
IARU Region 1
2m & 70cm Band Plan
Based on IARU-R1 VHF Handbook v9.00 November 2020
Ver 1.1
Sources:
National Authority for Management and Regulation in Communications of Romania - Radio amateur services regulations
ITU Radio Regulations, 2020 Edition
IARU-R1 VHF Handbook
YO3MIO - Feel free to print, distribute and modify this document while maintaining the source and author https://github.com/mircea84/VHFHamBands/
1 430.000 - 431.200 MHz not part of radio amateur service
432.000
432.500
433.000
433.600
435.000
438.000
430.375
431.625
431.050
Repeater in (7.6MHz shift)
Repeater in (1.6MHz shift)
432.500 New APRS
433.500 FM call
433.450 Digital voice call
433.400 SSTV
Repeater in (25kHz ch. / 2MHz shift)
Repeater out
(25kHz ch. / 1.6 or 2MHz shift)
434.600
Satellite service
Repeater out (7.6Mhz shift)
439.425
438.650
Repeater in (25kHz ch. / 1.6MHz shift)
432.493
432.100
432.400
Repeater out (1.6MHz shift)
431.2001
434.790
All modes
CW
MGM
SSB
FM / Dig. voice
Sat. service
ISM

## Slide 3
Frequency segment | Max Bw. (Hz) | Preferred mode and usage | 
430.000 - 431.975 | 20 kHz | All mode | 430.025 - 430.375 FM repeater output (1.6 MHz shift) 430.400 - 430.575 digital communications 430.600 . 430.925 digital communications repeater channels 430.925 - 431.025 multimode channels 431.050 - 431.825 Repeater input channel freqs 7.6 MHz shift 431.625 - 431.975 Repeater input channels (1.6MHz shift)
432.000 - 432.100 | 500 | MGM Telegraphy | 432.050 Telegraphy Centre of activity
432.100 - 432.400 | 2700 | MGM Telegraphy SSB | 432.200 SSB center of activity 432.350 Microwave talkback center of activity 432.370 Meteor Scatter center of activity
432.400 - 432.490 | 500 | MGM Telegraphy | Beacons Exclusive
432.491 -432.493 | 500 | EMGM | Experimental MGM
432.500 - 432.975 | 12 kHz | All mode | 432.500 New APRS frequency 432,600-432,9875 REPEATER INPUT REGION 1 STANDARD, 25 kHz spacing, 2 MHz shift (Channel freqs 432.600 - 432.975MHz)
433.000 -433.375 | 12 kHz | FM / Digital Voice repeaters | REPEATER INPUT REGION 1 STANDARD, 25 kHz spacing, 1.6 MHz shift
433.400 - 433.575 | 12 kHz | FM / Digital Voice | 433.400 SSTV (FM/AFSK) 433.450 Digital Voice calling 433.500 FM calling
433.600 - 434.000 | None | All mode | 433.625 - 433.775 Digital communications channels 434.000 Centre frequency of digital experiments
434.000 - 434.594 | 12 kHz | All mode - ATV | 434.450-434.575 Digital communications channels
434.594 - 434.981 | 12 kHz | All mode | 434.600-434.9875 Repeater Output (25 kHz spacing 1.6 or 2MHz shift)
435.000 -436.000 | None | Satellite service | 
436.000 -438.000 | None | Satellite service DATV/data | DATV/data center of activity
438.000 -440.000 | None | All mode | 438.025 - 438.175 Digital communication channels 438.200 - 438.525 Digital communication repeater channels 438.550 - 438.625 Multi mode 438.650 - 439.425 Repeater output channels (7.6 MHz shift) 439.800 - 439.975 Digital communication link channels
VHF 2m
144-146MHz (2MHz band)
UHF 70cm
430-440MHz (10MHz band)
Frequency segment | Max Bw. (Hz) | Preferred mode and usage | 
144.000 -144.025 | 2700 | All mode | sattelite downlink only
144.025 -144.100 | 500 | Telegraphy | 144.050 Telagraphy calling 144.100 Random MS
144.100 - 144.150 | 500 | MGM Telegraphy | 144.110-144.150 CW and MGM EME
144.150 - 144.400 | 2700 | SSB Telegraphy MGM | 144.195-144.205 Random MS SSB 144.300 SSB Centre of activity
144.400 - 144.490 | 500 | MGM Telegraphy | Beacons exclusive
144.491 - 144.493 | 500 | Personal weak signal MGM Beacons | Experimental MGM
144.500 - 144.794 | 20 kHz | All mode | 144.500 Image mode centre (SSTV, Fax,...) 144.600 Data Centre of activity (MGM, RTTY,..) 144.750 ATV Talk back
144.794 - 144.9625 | 12 kHz | MGM Digital Communication | 144.800 APRS 144.8125 DV internet voice gateway 144.8250 DV internet voice gateway 144.8375 DV internet voice gateway 144.8500 DV internet voice gateway 144.8625 DV internet voice gateway
144.975 - 145.194 | 12 kHz | FM/Digital Voice | Repeater input exclusive
145.194 - 145.206 | 12 kHz | FM/Digital Voice | Space Communication
145.206 - 145.5625 | 12 kHz | FM/Digital Voice | 145.2375 FM Internet Voice Gateway 145.2875 FM Internet Voice Gateway 145.3375 FM Internet Voice Gateway 145.375 digital voice calling 145.500 FM calling
145.575 - 145.7935 | 12 kHz | FM/Digital Voice | Repeater output exclusive
145.794 - 145.806 | 12 kHz | FM/Digital Voice | Space Communication
145.806 -146.000 | 12 kHz | All mode | Satellite exclusive
Based on IARU-R1 VHF Handbook v9.00 November 2020