## Slide 1
In countries without access to the full 70 cm band, the following 12.5 kHz repeater channels with a 1.6 MHz separation between uplink and downlink can be implemented:
a. Input Frequencies (uplink) 431.225 - 431.600 MHz
b. Output Frequencies (downlink) 432.825 - 433.200 MHz
 |  | VHF 2m | UHF 70cm
Authorized Peak Envelope Power (PEP) per class (W) | I | 400 | 200
 | II | 200 | 100
 | III | 100 | 50
 | IV | 50 | 30
VHF 2m
144 - 146 MHz (2 MHz band)
Satellite downlink only
144.050 CW center
144.300 SSB center
144.025
144.500
144.794
144.975
145.806
Satellite exclusive
145.800 ISS
145.575
Repeater out
145.206
145.500 FM Calling
144.800 APRS
145.194
Repeater in
Space Comm
145.794
Space Comm
UHF 70cm
430 - 440 MHz (10 MHz band)
IARU Region 1
2m & 70cm Band Plan
Ver 1.2
Based on IARU-R1 VHF Handbook v9.01 March 2021
Sources:
National Authority for Management and Regulation in Communications of Romania - Radio amateur services regulations
ITU Radio Regulations, 2020 Edition
IARU-R1 VHF Handbook
430.000 - 431.200 MHz not part of radio amateur service
432.491
432.100
432.400
Repeater in R1 (12.5 kHz / 7.6 MHz)
432.500 New APRS
433.500 FM call
433.450 Digital voice call
433.400 SSTV
Repeater in (25 kHz / 2 MHz)
Repeater out R1 (25 kHz / 1.6 or 2 MHz)
Satellite service
Digital comm
Repeater out (12.5 kHz / 1.6 MHz)
432.000
432.500
433.000
433.600
435.000
438.000
430.400
431.625
431.050
434.594
439.5875
438.650
434.790
145.225 FM Calling
144.174 FT8
144.050 Random MS
144.491
YO3MIO - Feel free to print, distribute and modify this document while maintaining the source and author Source documents here: https://github.com/mircea84/VHFHamBands/
Thanks radioamator.ro community for support!
All modes
CW
MGM
SSB
FM / Dig. voice
Sat. service
ISM
Beacons excl.
Modes:
See verso
20 kHz
12 kHz
None
Bandwidth:
Beacons
144.400
144.150
144.500 Image center
144.600 Data center
144.750 ATV talk back
430.600
Digital comm link
Digital comm repeater
430.925
Multimode
Repeater in (12.5 kHz / 1.6 MHz)
unavailable
431.200
432.050 CW center
432.200 SSB center
432.350 MW talkback center
432.370 MS center
432.600
Repeater out
433.400
Repeater in (25 kHz / 1.6 MHz)
Repeater out (25 kHz / 1.6 MHz)
434.000
434.000 Digital experim. center
434.775
Digital comm channels
LORA (125 kHz max bw)
Digital comm channels (by exception)
Repeater in (25 kHz / 1.6 MHz)
436.000
Satellite service
DATV / Data
437.000 DATV / Data center
438.200
438.550
439.800
Digital comm repeater
Multimode
Digital comm link
Repeater in R1 (12.5 kHz / 7.6 MHz)
Beacons

## Slide 2
Frequency segment (MHz) | Max Bw. | Mode | Usage
430.000 - 431.975 (national band planning) (*) |  | All modes | 430.025 - 430.375 FM repeater out (12.5 kHz spacing / 1.6 MHz shift) 430.400 - 430.575 Digital communications link (*) 430.600 - 430.925 Digital communications repeater channels (*) 430.925 - 431.025 Multimode channels (*) 431.050 - 431.825 Repeater in IARU-R1 (12.5 kHz spacing / 7.6 MHz shift) (*) 431.625 - 431.975 Repeater in (12.5 kHz spacing / 1.6 MHz shift) (*)
432.000 - 432.100 | 500 Hz | Telegraphy (*) MGM | 432.050 Telegraphy center of activity
432.100 - 432.400 | 2700 Hz | Telegraphy SSB MGM | 432.200 SSB center of activity 432.350 Microwave talkback center of activity 432.370 Meteor Scatter center of activity
432.400 - 432.490 | 500 Hz | Telegraphy MGM | Beacons exclusive (*)
432.491 -432.493 | 500 Hz | EMGM | Experimental MGM
432.500 - 432.975 | 12 kHz | All modes | 432.500 New APRS frequency 432.600 - 432.9875 Repeater in IARU-R1 (25 kHz spacing / 2 MHz shift) 432.600 - 432.975 UK - Repeater out
433.000 - 433.375 | 12 kHz | FM / Digital Voice repeaters (*) | 433.000 - 433.3875 Repeater in (12.5 kHz spacing / 1.6 MHz shift) (*) 433.000 - 433.375 UK Repeater out (25 kHz spacing / 1.6 MHz shift)
433.400 - 433.575 | 12 kHz | FM / Digital Voice (*) | 433.400 SSTV (FM/AFSK) 433.450 Digital Voice calling 433.500 FM calling Simplex channels 25 kHz spacing
433.600 - 434.000 |  | All modes | 433.625 - 433.775 Digital communications channels (*) 434.000 Centre frequency of digital experiments (*) LORA (*)
434.000 - 434.594 | 12 kHz (*) | All modes / ATV (*) | 434.450 - 434.575 Digital communications channels (by exception) (*)
434.594 - 434.981 | 12 kHz (*) | All modes | 434.600 - 434.9875 Repeater Out IARU-R1 (12.5 kHz spacing / 1.6 or 2 MHz shift) (*)
435.000 - 436.000 |  | Satellite service | 
436.000 - 438.000 |  | Satellite service DATV / data (*) | 437.000 DATV / data center of activity
438.000 - 440.000 |  | All modes | 438.025 - 438.175 Digital communication channels (*) 438.200 - 438.525 Digital communication repeater channels (*) 438.550 - 438.625 Multimode channels (*) 438.650 - 439.425 Repeater out IARU-R1 (12.5 kHz / 7.6 MHz shift) (*) 439.800 - 439.975 Digital communication link channels (*)
VHF 2m
144-146 MHz (2 MHz band)
UHF 70cm
430-440 MHz (10 MHz band)
Frequency segment (MHz) | Max Bw. | Mode | Usage
144.000 -144.025 | 2700 Hz | All modes | Satellites downlink only (*)
144.025 -144.100 | 500 Hz | Telegraphy (*) | 144.050 Telegraphy calling 144.100 Random MS (*)
144.100 - 144.150 | 500 Hz | Telegraphy MGM | 144.110-144.160 CW and MGM EME (*)
144.150 - 144.400 | 2700 Hz | Telegraphy SSB MGM | 144.300 SSB center of activity
144.400 - 144.490 | 500 Hz | Telegraphy MGM | Beacons exclusive (*)
144.491 - 144.493 | 500 Hz | Personal weak signal MGM Beacons | Experimental MGM
144.500 - 144.794 | 20 kHz | All mode (*) | 144.500 Image mode center (SSTV, Fax,...) 144.600 Data center of activity (MGM, RTTY,..) 144.750 ATV talk back
144.794 - 144.9625 | 12 kHz | MGM (*) Digital communications | 144.800 APRS 144.8125 DV internet voice gateway 144.8250 DV internet voice gateway 144.8375 DV internet voice gateway 144.8500 DV internet voice gateway 144.8625 DV internet voice gateway
144.975 - 145.194 | 12 kHz | FM / Digital Voice | Repeater input exclusive (*)
145.194 - 145.206 | 12 kHz | FM / Digital Voice (*) | Space Communication (*)
145.206 - 145.5625 | 12 kHz | FM / Digital Voice (*) | 145.2375 FM Internet voice gateway 145.2875 FM Internet voice gateway 145.3375 FM Internet voice gateway 145.375 Digital voice calling 145.500 FM calling
145.575 - 145.7935 | 12 kHz | FM / Digital Voice | Repeater output exclusive (*)
145.794 - 145.806 | 12 kHz | FM / Digital Voice (*) | Space communication (*)
145.806 -146.000 | 12 kHz | All modes (*) | Satellite exclusive
Based on IARU-R1 VHF Handbook v9.01 March 2021
(*) See notes from Handbook

## Slide 3
MS - Meteor Scatter
MGM – Machine Generated Mode
EMGM -
EME – Earth Moon Earth
CW – Continuous Wave – Morse code
SSB – Single Side Band
ATV – Amateur Television
DATV
SSTV
RTTY
FT8
DV – Digital Voice
APRS
FM
F/PA/ON ??

## Slide 4
VHF 2m
144-146MHz (2MHz band)
Satellite Downlink
144.050 CW calling
144.300 SSB Center
144.025
144.500
144.794
144.975
145.806
Satellite exclusive
145.800 ISS
145.575
Repeater out
145.206
145.500 FM Calling
144.800 APRS
145.194
Repeater in
Space Comm
145.794
Space Comm
UHF 70cm
430-440MHz (10MHz band)
See verso
20 kHz
12 kHz
none
 | Authorized Peak Envelope Power (PEP) per class (W) |  |  | 
 | I | II | III | IV
VHF - 2m | 400 | 200 | 100 | 50
UHF - 70cm | 200 | 100 | 50 | 30
IARU Region 1
2m & 70cm Band Plan
Based on IARU-R1 VHF Handbook v9.00 November 2020
Ver 1.1
Sources:
National Authority for Management and Regulation in Communications of Romania - Radio amateur services regulations
ITU Radio Regulations, 2020 Edition
IARU-R1 VHF Handbook
YO3MIO - Feel free to print, distribute and modify this document while maintaining the source and author https://github.com/mircea84/VHFHamBands/
1 430.000 - 431.200 MHz not part of radio amateur service
432.000
432.500
433.000
433.600
435.000
438.000
430.375
431.625
431.050
Repeater in (7.6MHz shift)
Repeater in (1.6MHz shift)
432.500 New APRS
433.500 FM call
433.450 Digital voice call
433.400 SSTV
Repeater in (25kHz ch. / 2MHz shift)
Repeater out
(25kHz ch. / 1.6 or 2MHz shift)
434.600
Satellite service
Repeater out (7.6Mhz shift)
439.425
438.650
Repeater in (25kHz ch. / 1.6MHz shift)
432.493
432.100
432.400
Repeater out (1.6MHz shift)
431.2001
434.790
All modes
CW
MGM
SSB
FM / Dig. voice
Sat. service
ISM

## Slide 5
VHF 2m
144 - 146 MHz (2 MHz band)
Satellite downlink only
144.050 CW center
144.300 SSB center
144.025
144.500
144.794
144.975
145.806
Satellite exclusive
145.800 ISS
145.575
Repeater out
145.206
145.500 FM Calling
144.800 APRS
145.194
Repeater in
Space Comm
145.794
Space Comm
UHF 70cm
430 - 440 MHz (10 MHz band)
 | Authorized Peak Envelope Power (PEP) per class (W) |  |  | 
 | I | II | III | IV
VHF - 2m | 400 | 200 | 100 | 50
UHF - 70cm | 200 | 100 | 50 | 30
IARU Region 1
2m & 70cm Band Plan
Ver 1.2
Based on IARU-R1 VHF Handbook v9.01 March 2021
Sources:
National Authority for Management and Regulation in Communications of Romania - Radio amateur services regulations
ITU Radio Regulations, 2020 Edition
IARU-R1 VHF Handbook
430.000 - 431.200 MHz not part of radio amateur service
432.491
432.100
432.400
Repeater in R1 (12.5 kHz / 7.6 MHz)
432.500 New APRS
433.500 FM call
433.450 Digital voice call
433.400 SSTV
Repeater in (25 kHz / 2 MHz)
Repeater out R1 (25 kHz / 1.6 or 2 MHz)
Satellite service
Digital comm
Repeater out (12.5 kHz / 1.6 MHz)
432.000
432.500
433.000
433.600
435.000
438.000
430.400
431.625
431.050
434.594
439.5875
438.650
434.790
145.225 FM Calling
144.174 FT8
144.050 Random MS
144.491
YO3MIO - Feel free to print, distribute and modify this document while maintaining the source and author Source documents here: https://github.com/mircea84/VHFHamBands/
Thanks radioamator.ro community for support!
All modes
CW
MGM
SSB
FM / Dig. voice
Sat. service
ISM
Beacons excl.
Modes:
See verso
20 kHz
12 kHz
None
Bandwidth:
Beacons
144.400
144.150
144.500 Image center
144.600 Data center
144.750 ATV talk back
430.600
Digital comm link
Digital comm repeater
430.925
Multimode
Repeater in (12.5 kHz / 1.6 MHz)
unavailable
431.200
432.050 CW center
432.200 SSB center
432.350 MW talkback center
432.370 MS center
432.600
Repeater out
433.400
Repeater in (25 kHz / 1.6 MHz)
Repeater out (25 kHz / 1.6 MHz)
434.000
434.000 Digital experim. center
434.775
Digital comm channels
LORA (125 kHz max bw)
Digital comm channels (by exception)
Repeater in (25 kHz / 1.6 MHz)
436.000
Satellite service
DATV / Data
437.000 DATV / Data center
438.200
438.550
439.800
Digital comm repeater
Multimode
Digital comm link
Repeater in R1 (12.5 kHz / 7.6 MHz)
Beacons
In countries without access to the full 70 cm band, the following 12.5 kHz repeater channels with a 1.6 MHz separation between uplink and downlink can be implemented:
a. Input Frequencies (uplink) 431.225 - 431.600 MHz
b. Output Frequencies (downlink) 432.825 - 433.200 MHz